TESTCASE DOC

# DIRECT CASE

Path :
/branches/dev_lilian/DassFlow_varchg/cases/sw_mono/bin_channel_straight/rundirect/

## Simulation and numerical params

Readable directly in /branches/dev_lilian/DassFlow_varchg/cases/sw_mono/bin_channel_straight/rundirect/input.txt

## Mesh description
Rectangular mesh :
- Length = 1000m
- width = 100m
- nb node = 1000
- nb cells = 891 (9 *99)

irregular splope →

no variation along the width (y axis)

y

x

## Boundary conditions

### Qin

### Rating curve

## Complementary info for the test case

Manning is uniform : n= 0,05

## Observed stations

4 observed points
- points 1 and 2 take a single measure
- Points 3 and 4 are defined in stations_grp_xxxx.txt → it gives one observed value (ie the mean of the 9 points considered ? → Need to be confirmed)

# PRIOR data for minimisation
Path :
/branches/dev_lilian/DassFlow_varchg/cases/sw_mono/bin_channel_straight/prior_data/

## Qin :

Qin = constant = 100m³/s
## Bathy :
Straight slope here

## Manning :

n=0.5